## Slide 1
PROJECT GUIDANCE · DEGGENDORF INSTITUTE OF TECHNOLOGY
Driver Safety
Vision System — IMX500 Edition
A real-time, on-sensor AI monitoring system that watches for phone distraction, drowsiness, and masked-eye stillness — and alerts the driver before it's too late.
Phone distraction
Drowsiness (EAR)
Sunglasses + stillness
Raspberry Pi 5 · Sony IMX500 AI Camera · MediaPipe · Ultralytics YOLO

## Slide 2
Project Overview
A real-time driver monitoring pipeline running entirely on a Raspberry Pi with the Sony IMX500 AI camera.
Phone Distraction
IMX500 on-sensor object detection flags a COCO “cell phone” held near the driver's face.
Beep after 2s
Drowsiness (Eyes)
MediaPipe FaceMesh tracks the Eye Aspect Ratio (EAR) across 6 landmarks per eye.
Beep after 2s
Sunglasses + Stillness
When EAR is unreliable, MediaPipe Holistic tracks nose movement instead.
Voice → beep
Driver Safety Vision System — IMX500 Edition
02

## Slide 3
Hardware & Software Stack
Everything runs locally on-device — no cloud inference required.
Hardware
Raspberry Pi 5 (tested platform)
Raspberry Pi AI Camera — Sony IMX500
Speaker / audio output for beep + TTS alerts
Software
Python 3.10 — required for the IMX500 toolchain
Picamera2 — camera & IMX500 interface
MediaPipe — FaceMesh & Holistic landmarks
OpenCV — frame processing & overlays
espeak — text-to-speech voice prompts
paplay / PulseAudio — beep alerts
Driver Safety Vision System — IMX500 Edition
03

## Slide 4
System Architecture
From camera frame to driver alert, end to end.
1
Capture
Picamera2 grabs the live frame
2
On-sensor inference
IMX500 runs the detection model
3
Landmark tracking
MediaPipe FaceMesh / Holistic
4
Driver selection
Largest box = closest = driver
5
Alert
Beep / voice prompt if triggered
Driver selection logic: when multiple people are visible, the system keeps only the largest bounding box per class (closest to camera) as the driver. Boxes smaller than MIN_DRIVER_BOX_AREA = 4000 px² are treated as background.
Driver Safety Vision System — IMX500 Edition
04

## Slide 5
01 Phone Distraction
How it works
The IMX500 detects “cell phone” objects on-sensor. If a phone is found near the driver's face for longer than the time limit, an audible alert fires.
Horizontal distance < PHONE_FACE_DIST (200 px)
Vertical difference < PHONE_FACE_VDIFF (120 px)
Condition held for ≥ PHONE_TIME_LIMIT (2.0 s)
Alert: beep fires once the 2-second threshold is crossed
PHONE_FACE_DIST
200 px
PHONE_TIME_LIMIT
2.0 sec
Driver Safety Vision System — IMX500 Edition
05

## Slide 6
02 Drowsiness — Eye Aspect Ratio
MediaPipe FaceMesh extracts 6 landmarks per eye. The Eye Aspect Ratio (EAR) measures how open the eyes are — it drops sharply when eyes close.
EAR = ( |p2−p6| + |p3−p5| ) ÷ ( 2 × |p1−p4| )
Skipped automatically when sunglasses are detected
Averaged across both left and right eye
Reset the moment eyes reopen — no lingering alert
EAR_THRESHOLD
< 0.20
eyes considered closed
EYE_TIME_LIMIT
2.0 sec → alert
Driver Safety Vision System — IMX500 Edition
06

## Slide 7
03 Sunglasses + Head Stillness
When sunglasses make eye-tracking unreliable, the system falls back to nose-movement tracking via MediaPipe Holistic.
Stage 1
Sunglasses detected
IMX500 sunglasses class fires; EAR check is paused.
Stage 2
5 seconds still
Nose moves < 3 px/frame for STILL_VOICE_DELAY = 5.0 s.
Stage 3
Voice prompt
“Hello, how are you doing?” plays via espeak TTS.
Stage 4
3s later → beep
No response after POST_VOICE_DELAY = 3.0 s triggers a beep.
MOVEMENT_THRESHOLD = 3 px defines “not moving.” If the driver moves before the voice prompt or beep fires, the whole sequence resets immediately — including the per-channel beep cooldown.
Driver Safety Vision System — IMX500 Edition
07

## Slide 8
Key Thresholds
All tunable constants live at the top of driver_safety.py.
Constant | Value | Meaning
EAR_THRESHOLD | 0.20 | EAR below this → eyes closed
PHONE_TIME_LIMIT | 2.0 s | Phone near face before alert
EYE_TIME_LIMIT | 2.0 s | Eyes closed before drowsy alert
STILL_VOICE_DELAY | 5.0 s | Stillness before voice prompt
POST_VOICE_DELAY | 3.0 s | After voice, before beep
MOVEMENT_THRESHOLD | 3 px | Pixel delta = “not moving”
PHONE_FACE_DIST | 200 px | Max distance for “phone near face”
MIN_DRIVER_BOX_AREA | 4000 px² | Min box area to count as driver
BEEP_COOLDOWN | 2.0 s | Seconds between repeated beeps
Driver Safety Vision System — IMX500 Edition
08

## Slide 9
Training a Custom Model
Fine-tuning YOLOv8n on three domain-specific classes using Google Colab.
3 Classes
0
phone
Cell phone near face
1
face
Driver's face
2
sunglasses
Worn by driver
Sunglasses are oversampled ×8 to correct class imbalance before the 80/10/10 train/val/test split.
Training configuration (YOLOv8n)
epochs | 200 | patience | 50
imgsz | 640 | batch | 16
degrees | 10 | translate | 0.05
scale | 0.5 | shear | 2
fliplr | 0.5 | mosaic | 0.7
mixup | 0.15 | copy_paste | 0.4
Output: best.pt — saved to /content/DSVS_training/driver_monitoring/ and auto-downloaded for IMX500 export. The IMX500 supports only YOLOv8n and YOLO11n.
Driver Safety Vision System — IMX500 Edition
09

## Slide 10
Export & Deployment Pipeline
From trained weights to running inference on the IMX500 sensor.
Colab
1
Train
Fine-tune YOLOv8n on phone / face / sunglasses
best.pt
Linux only · Py 3.10
2
Export to IMX
yolo_export.py --export_format imx --int8_weights
packerOut.zip
Raspberry Pi
3
Package to RPK
imx500-package -i packerOut.zip -o ./model_output
network.rpk
Raspberry Pi
4
Run
uv run python driver_safety.py --model network.rpk
Live inference
Driver Safety Vision System — IMX500 Edition
10

## Slide 11
Robustness & Alert Logic
Two engineering details that keep alerts accurate and responsive.
Multi-Person Robustness
When several people appear in frame (passengers, pedestrians), the system buckets detections by class and keeps only the largest bounding box — the person closest to the camera, i.e. the driver.
MIN_DRIVER_BOX_AREA
4000 px²
Per-Channel Beep Cooldown
Phone, eye, and sunglasses alerts each track their own 2-second cooldown. The instant a condition clears, its cooldown resets to zero — so the next genuine alert beeps immediately, with no stale delay.
BEEP_COOLDOWN
2.0 sec × 3 channels
Driver Safety Vision System — IMX500 Edition
11

## Slide 12
Built On
Acknowledgements
Picamera2
Camera interface & IMX500 integration
MediaPipe
FaceMesh and Holistic landmark detection
Ultralytics YOLO
Model training and export
Sony IMX500
On-sensor AI inference
Project guidance by Prof. Dr. Thomas Ewender
Deggendorf Institute of Technology